## Slide 1: Misapplications of CMFs
Karen Scurry and Daniel Carter
CMF Clearinghouse Webinar
Dec 17, 2018

## Slide 2: Introduction
Selecting an appropriate CMF is important – information on previous webinar
Applying CMFs correctly is important as well – can have large impact on results
CMF Clearinghouse team is available to help explain CMFs on the site or from a study report
Examples of misapplications

## Slide 3: CMF Misapplications
Clearly right
Clearly wrong
In an ideal world, it would always be obvious when CMFs were applied correctly and when they were applied incorrectly.
Notes: We’d like to think that it’s always obvious when CMFs are or are not being correctly applied.

## Slide 4: CMF Misapplications
Clearly right
Clearly wrong
Minor concerns
Major concerns
In reality, there is often a grey area, where CMFs might have been applied appropriately, but the application may have some minor or major concerns.
Notes: The truth is that sometimes it’s hard to tell. Need to understand the issues involved. Many times it can be a judgement call based on best information available.

## Slide 5: CMF Misapplications
Calculating CMF incorrectly
Applying CMF to wrong crash type
Inappropriately applying CMFs as SPF adjustment factors
Applying too many CMFs without accounting for interrelationship of effect

## Slide 6: CMF Misapplications
All examples based on real encounters
Names and numbers changed to protect the innocent (or guilty)

## Slide 7: Calculating CMF Incorrectly

## Slide 8: Calculating CMF Incorrectly
An engineer considered realigning an intersection from the current 75 degree angle to 90 degrees

## Slide 9: Calculating CMF Incorrectly
Research study indicates a CMF of 1.48 for a 75 degree intersection compared to a 90 degree intersection
Engineer’s question: “Would it be logical to assume if this intersection was realigned to 90 degrees that the crash rate would then drop by 52 percent?”

## Slide 10: Calculating CMF Incorrectly
Clearly wrong

## Slide 11: Calculating CMF Incorrectly
Mistake: assuming that a 1.48 CMF would lead to a 52% reduction in crashes (presumably because 2.0-1.48=0.52?)
This represents an expected 32% reduction in crashes (100-100x0.68 = 32), not 52%
CMF = (CMF for new condition) / (CMF for old condition)
= (CMF for 90 degrees) / (CMF for 75 degrees)
= 1.00 / 1.48 = 0.68.

## Slide 12: Applying CMF to Wrong Crash Type

## Slide 13: Applying CMF to Wrong Crash Type
Situation: Deficient vertical curve (K value that does not meet AASHTO design standard)
Observed 5-year crash history shows 50 crashes (0 fatal, 3 A-injury, 5 B-injury, 15 C-injury, 27 PDO)
Engineer determines that 10 of these crashes (2 per year) are related to the vertical curve design

## Slide 14: Applying CMF to Wrong Crash Type
Engineer identified a CMF of 0.49 for improving vertical alignment. As shown below, the CMF applies to KABC crashes of all types.

## Slide 15: Applying CMF to Wrong Crash Type
Engineer applied the CMF to the identified target crashes
2 average crashes per year x 0.49 = 1 average crashes per year after realignment
Benefit was calculated as preventing 1 target crash per year

## Slide 16: Applying CMF to Wrong Crash Type
Clearly wrong
Notes: The truth is that sometimes it’s hard to tell. Need to understand the issues involved. Many times it can be a judgement call based on best information available.

## Slide 17: Applying CMF to Wrong Crash Type
To apply correctly: apply the CMF to the KABC crashes.
3 A-injury, 5 B-injury, 15 C-injury over 5 years = 4.6 KABC crashes per year
Benefit is preventing 2.3 KABC crashes per year
NOTE: It would be better to use SPF and EB adjustment to calculate expected crashes instead of using observed crashes
4.6 x 0.49 = 2.3 KABC average crashes per year after realignment

## Slide 18: Inappropriately Applying CMFs as SPF Adjustment Factors

## Slide 19: Inappropriately Applying CMFs as SPF Adjustment Factors
Sometimes site characteristics or desired changes are not accounted for in SPFs
Standalone CMFs can be used to adjust predicted results, however…
Must match base conditions
  Site characteristics
  Crash type distributions
Must not overapply multiple CMFs

## Slide 20: Inappropriately Applying CMFs as SPF Adjustment Factors
An agency was weighing options for widespread safety enhancements and the anticipated benefits
Analysts used CMFs to adjust crash predictions for many locations across the agency’s jurisdiction
CMFs came from standalone countermeasures featured in the Clearinghouse

## Slide 21: Inappropriately Applying CMFs as SPF Adjustment Factors
Minor concerns
Major concerns

## Slide 22: Inappropriately Applying CMFs as SPF Adjustment Factors
Could be appropriate at some locations but inappropriate at others
Most of the anticipated benefit came from estimates from standalone CMFs rather than factors in the SPF

## Slide 23: Inappropriately Applying CMFs as SPF Adjustment Factors
Standalone CMFs may not have matched base condition of the SPF in terms of site characteristics
Standalone CMFs may not have been a good match to some sites based on crash type patterns
  If a countermeasure was intended for a target crash type, but the author reported a CMF developed for total crashes
  Would likely have a different effect on total crashes if applied at a location with a substantially lower proportion of the target crash type

## Slide 24: Inappropriately Applying CMFs as SPF Adjustment Factors
Potential for overreach in applying standalone CMFs (i.e., over estimating benefit of treatments by applying too many CMFs)

## Slide 25: Applying too many CMFs without accounting for interrelationship of effect

## Slide 26: Applying too many CMFs without accounting for interrelationship of effect
A state agency created a spreadsheet for calculating the anticipated benefits of safety projects
The form allowed 10 countermeasures to be included, each with its own CMF
In this tool, each CMF would contribute to the anticipated crash reduction

## Slide 27
Major concerns
Applying too many CMFs without accounting for interrelationship of effect

## Slide 28: Applying too many CMFs without accounting for interrelationship of effect
CMFs may address the same crash type
For example, addressing run off road crashes at curves
  Chevrons
  Wider edgelines
  High friction surfacing
The effects are related (not independent)

## Slide 29: Applying too many CMFs without accounting for interrelationship of effect
Multiplying CMFs together likely overstates benefit, especially when considering many countermeasures
A tool (or analyst) must account for interrelationship of effect
Conservative approach: Use CMF from only the most effective treatment
More guidance forthcoming in the Highway Safety Manual, 2nd edition using results from NCHRP 17-63