## Slide 1: Application of Multiple CMFs
Frank Gross, VHB

## Slide 2: Questions
Can you use CMFs to estimate the combined effect of multiple countermeasures?
What methods should you use?
  Add CMFs?
  Multiply CMFs?
  Other methods?

## Slide 3: Ideal Answer
Apply CMF that represents combined effect
Examples of CMFs for Combined Countermeasures | CMF | Star Rating | CMF ID
Install shoulder rumble strips and widen shoulder | 0.61 | 4-star | 6665
Install centerline and shoulder rumble strips | 0.80 | 5-star | 6850
Install a traffic signal and left turn lanes | 0.57 | 4-star | 7967
Install raised median with marked crosswalk | 0.54 | 3-star | 175

## Slide 4: In an Unideal World
Estimate combined effect using CMFs that represent individual countermeasure effects
Countermeasure 1 | CMF 1 | CMF ID | Countermeasure 2 | CMF 2 | CMF ID | Combined Effect
Install left-turn lane | 0.72 | 260 | Improve intersection sight distance | 0.63 | 1638 | ?
Install two-way-left-turn lane | 0.80 | 2341 | Reduce driveway density from 15 to 10 per mile | 0.89 | 2248 | ?
Install high-visibility crosswalk | 0.60 | 4123 | Implement leading pedestrian interval | 0.87 | 9918 | ?

## Slide 5: Potential Methods
Methods to Estimate Combined Effect of Multiple Countermeasures | 
Multiplicative | *CMF1 = most effective countermeasure
Additive | *maximum reduction = 100% (i.e., CMF = 0)
Dominant effect | *only consider countermeasure with smallest CMF
Dominant common residuals | 
Methods to Estimate Combined Effect of Multiple Countermeasures | 
Multiplicative | 
Additive | 
Dominant effect | 
Dominant common residuals | 

## Slide 6: Method Selection Process
Define scenario of interest
Understand limits of combined countermeasure effect
Determine potential for overlapping effects among countermeasures
Categorize magnitude of individual countermeasure effects

## Slide 7: 1. Define Scenario of Interest
Countermeasures
Roadway characteristics
Traffic volume
Crash type and severity
Time of day
Specific treatment location

## Slide 8: 2. Understand Limits of Combined Effect
1+1 = 2 | 1-1 = 0
1-1-1 = -1 | 1+1 = 3

## Slide 9: 3. Determine Potential for Overlapping Effects
Defined with respect to target crashes
  Represents likelihood that individual countermeasures would address similar crashes
Different than applicability of CMF
  Reflects crash types used to develop CMF

## Slide 10: 3. Determine Potential for Overlapping Effects
Convert intersection with minor-road stop control to roundabout | 
CMF | 0.13
Crash Type | All
Crash Severity | Injury
Area Type | Rural
CMF ID | 230

## Slide 11: 3. Determine Potential for Overlapping Effects
Scenario
Location: 2-way, stop-controlled intersection
CM1: install lighting on major road
CM2: install intersection warning signs on minor road
Question
Do you think there would be no overlap, some overlap, or complete overlap in the target crashes?

## Slide 12: 3. Determine Potential for Overlapping Effects
Potential Overlap
Zero Overlap
Complete Overlap
Some Overlap
Enhancing Effects
Counteracting Effects

## Slide 13: 3. Determine Potential for Overlapping Effects

## Slide 14: 4. Categorize Magnitude of Individual Effects
Individual Effect | Assigned Magnitude
< 10% change | Small
10 – 25% change | Medium
> 25% change | Large

## Slide 15: Select Method to Estimate Combined Effect (CMFs apply to same crash type and severity)
Magnitude | Overlap | Method
One or more CMFs > 1.0 | Not Applicable | Multiplicative
Both CMFs < 1.0 | Zero Overlap or Enhancing Effects | Additive
 | Complete Overlap | Dominant effect
 | Some Overlap | Dominant effect OR Dominant common residuals; whichever produces greatest reduction (i.e., smallest combined CMF)

## Slide 16: Example Application
Countermeasure | CMF | Applicable Crash Type | Applicable Severity | Applicable Facility Type | CMF ID
Install two-way-left-turn lane | 0.80 | All | All | Rural, 2-lane roads | 2341
Reduce driveway density from 15 to 10 driveways per mile | 0.89 | All | All | All 2-lane roads | 2248

## Slide 17: Select Method to Estimate Combined Effect (CMFs apply to different crash type or severity)
Apply smallest CMF to applicable crashes
  Excluding crashes associated with other CMFs
Apply next smallest CMF to applicable crashes
  Excluding crashes associated with other CMFs
If necessary, estimate CMF for combined effect and apply it to applicable crashes
Sum change in crashes to calculate combined effect
Check that estimated change ≤ 100%

## Slide 18: Example Application
Crash Group2
Crash Group1
CMF1
CMF2
Total Crashes = X-median + ROR-right + S.S. same direction |  |  | 
Crashes Without (9 total) | Crash Group 1 (3 X-median) | Crash Group 2 (4 ROR-right) | Crash Group 3 (2 S.S. same)
CMF 1 applies to X-median crashes; CMF 2 applies to ROR-right crashes |  |  | 
CMF1 | 0.87 | -- | --
CMF2 | -- | 0.93 | --
Crashes With | CMF 1 * C.G. 1 0.87 * 3 = 2.61 | CMF 2 * C.G. 2 0.93 * 4 = 3.72 | 2 S.S. same no CMFs, no change
Difference | 3 – 2.61 = 0.39 | 4 – 3.72 = 0.28 | 2 – 2 = 0
Combined Countermeasure Effect = 0.39 + 0.28 + 0 = 0.67 Confirm this is ≤ Total Crashes (0.67 < 9; confirmed!)

## Slide 19: Example Application
Crash Group3
Crash Group2
Crash Group1
CMF1
CMF2
Crash Group2
Crash Group3
Crash Group1
CMF1
CMF2
Crash Group2
Crash Group1
CMF1
CMF2

## Slide 20: Questions
Can you use CMFs to estimate the combined effect of multiple countermeasures?
What methods should you use?
  Add CMFs?
  Multiply CMFs?
  Other methods?

## Slide 21: Questions
Frank Gross
VHB
919-334-5602
fgross@vhb.com